## Slide 1: Calcium Assessment: Autodetection
Optimized with OCT

## Slide 2: Calcium Augmentation Enabled
CALCIUM AUTODETECTION
  Calcium is indicated in orange
  Orange arc around the cross-sectional view indicates calcium in the current frame
    Arc is calculated from the lumen center (orange crosshair)
    Arc is displayed when calcium angle is at or above 60 degrees of circumferential calcium
Information contained herein for DISPLAY in Australia and New Zealand ONLY.
©2022 Abbott. All rights reserved. MAT-2212892 v1.0
Ultreon™ 1.0 Software Instructions For Use (IFU). Refer to IFU for additional information.

## Slide 3: Calcium Augmentation Enabled (cont.)
CALCIUM AUTODETECTION (cont.)
  Maximum thickness of calcium in the current frame indicated by white triangle
  Lumen profile highlights frames with total calcium angle that exceeds user-defined threshold
  Co-registration view allows user to visualize calcium on angio still-frame
  Note: Physician threshold preference for calcium detection is available under System Settings - Physician Profiles
Information contained herein for DISPLAY in Australia and New Zealand ONLY.
©2022 Abbott. All rights reserved. MAT-2212892 v1.0
Ultreon™ 1.0 Software Instructions For Use (IFU). Refer to IFU for additional information.

## Slide 4: Calcium Augmentation Disabled
CALCIUM AUTODETECTION Disabled
  Turning off Augmentation will remove the highlighted overlays displays on the images
  The cut plane on the 2D cross sectional image is now displayed with augmentation off, which allows the user to rotate the longitudinal view
  Total angle of calcium and thickness value remains
Information contained herein for DISPLAY in Australia and New Zealand ONLY.
©2022 Abbott. All rights reserved. MAT-2212892 v1.0
Ultreon™ 1.0 Software Instructions For Use (IFU). Refer to IFU for additional information.

## Slide 5: Calcium Autodetection Assessment
VIDEO
Information contained herein for DISPLAY in Australia and New Zealand ONLY.
©2022 Abbott. All rights reserved. MAT-2212892 v1.0
Ultreon™ 1.0 Software Instructions For Use (IFU). Refer to IFU for additional information.

## Slide 6: Treatment Strategy1-4
  Use clinical judgment to evaluate best strategy for non-calcific plaque.
  If calcium length is also > 5 mm, consider vessel preparation with NC Balloon; Cutting/Scoring Balloon; Atherectomy, or IVL1,4
LOW CALCIUM
HIGH CALCIUM
NO CALCIUM
Information contained herein for DISPLAY in Australia and New Zealand ONLY.
©2022 Abbott. All rights reserved. MAT-2212892 v1.0
All references available on slide 7.
Page 6 of 9

## Slide 7: References
Taylor, A., et al. Efficacy and Safety of Direct Stenting in Coronary Angioplasty, J. Invasive Cardiology, 2000; 12(11).
Romagnoli, E., et al. Drug Eluting Stenting, JACC Cardiovascular Interventions, 2008; 1(1): 21-31.
Seyithan Oglu, B., Compliant vs Non-compliant balloons. A Prospective Randomised Study, 1998; 39(1): 45-54.
Tomey, M., Current Status of Rotational Atherectomy, JACC Cardiovascular Interventions, 2014; 7(4): 345-354.
Information contained herein for DISPLAY in Australia and New Zealand ONLY.
©2022 Abbott. All rights reserved. MAT-2212892 v1.0
Page 7 of 9

## Slide 8
Page 8 of 9
CAUTION: This product is intended for use by or under the direction of a physician. Prior to use, reference the Instructions for Use, inside the product carton (when available) or at vascular.eifu.abbott or at medical.abbott/manuals for more detailed information on Indications, Contraindications, Warnings, Precautions and Adverse Events. This material is intended for use with healthcare professionals only.
Illustrations are artist’s representations only and should not be considered as engineering drawings or photographs. Photos on file at Abbott.
Information contained herein for DISPLAY in Australia and New Zealand ONLY.
Abbott Vascular division of Abbott Medical New Zealand Ltd, Grd Flr, Bldg. D, 4 Pacific Rise Mt Wellington, Auckland 1060 Tel: 0800 827 285
Abbott Vascular division of Abbott Medical Australia Pty Ltd, 299 Lane Cove Road, Macquarie Park NSW 2113, Tel: 1800 550 939
™ Indicates a trademark of the Abbott Group of Companies
www.cardiovascular.abbott/au/en
©2022 Abbott. All rights reserved. MAT-2212892 v1.0